## Slide 1
Real-Time DeepJSCC-Q on FPGA
Wireless image transmission on two Zynq boards
30 fps
256 × 256 RGB
18,020 frames in 600 s
67.5 ms
PL frame latency
Frames overlap in the pipeline
+2.8 dB
High-SNR PSNR gain over SSCC
DIV2K 0802; equal symbol budget
Two-board wireless link
RX (left), TX (right).
2 × PYNQ-ZU + 2 × AD-FMCOMMS3.
TX board
RX board
Camera/video
RGB input
CNN encoder
64-QAM symbols
OFDM TX
Buffer + IFFT
AD9361
915 MHz
Touch screen
Image + PHY
CNN decoder
Soft I/Q
OFDM RX
Sync + equalize
AD9361
Fast AGC
air
32,768 complex symbols/image
683 OFDM symbols/frame
20 MSPS PHY sample rate
Soft I/Q enters the decoder without hard decisions. Ethernet carries control and the reference preview.
PL latency excludes app/display.
Transfer includes buffers + RX PHY.
Measured quality over the air
DIV2K 0802; same PHY and 32,768 symbols/image.
SSCC: JPEG + 802.11n LDPC + 64-QAM.
Chart: PSNR (dB)
| 2.94 | 4.94 | 5.9 | 7.03 | 8.43 | 9.3 | 10.49 | 11.48 | 12.48 | 13.02 | 13.74 | 14.18 | 15.76 | 16.33 | 17.03 | 17.36 | 17.38 | 18.45 | 18.91 | 19.54 | 19.68 | 20.79 | 21.31 | 22.48 | 23.1 | 23.24 | 24.49 | 26.5 | 27.69 | 29.56 | 31.97 | 34.43 | 35.2 | 36.14 | 36.49
DeepJSCC-Q | 23.51 | 25.58 | 26.94 | 28.22 | 29.1 | 29.77 | 30.4 | 30.72 | 30.96 | 31.01 | 31.22 | 31.46 | 31.49 | 31.68 | 31.74 | 31.79 | 31.8 | 31.87 | 31.91 | 31.94 | 31.95 | 32 | 32.03 | 32.07 | 32.09 | 32.1 | 32.13 | 32.16 | 32.17 | 32.19 | 32.2 | 32.21 | 32.21 | 32.21 | 32.21
SSCC | 9.62 | 9.54 | 9.59 | 9.65 | 9.64 | 14.04 | 9.5 | 9.12 | 9.34 | 27.78 | 28.3 | 28.15 | 25.04 | 28.99 | 29.18 | 29.34 | 29.42 | 29.42 | 29.42 | 29.42 | 29.42 | 29.34 | 29.42 | 29.42 | 29.42 | 29.42 | 29.42 | 29.42 | 29.42 | 29.42 | 29.42 | 29.42
Original
256 × 256
RGB
Reconstruction at four channel conditions
36.1 dB
14.2 dB
10.5 dB
2.9 dB
DeepJSCC-Q
SSCC
32.21 / 0.94
31.46 / 0.94
30.41 / 0.93
23.51 / 0.77
29.42 / 0.86
14.33 / 0.63
9.48 / 0.16
No decodable
frame
N/A
Matched TX attenuation; column SNR of the DeepJSCC-Q frames.
Curve: window means. Images: frame PSNR (dB) / SSIM.
Decode failures are scored as mid-gray.
Streaming FPGA implementation
250 MHz, W8A12, 1.15 GMAC/frame
Line buffer
K or K+1 rows
Window
K × K × Cin
P MAC lanes
P accumulators
Requantize
Bias, act., shift
Weight ROM
Layer engines form a pipeline; P meets 30 fps.
On-chip buffers avoid full intermediate feature maps.
Routed TX / RX totals on xczu5eg
Design | LUT | BRAM36 | URAM | DSP
TX | 54,246 | 104.5 | 10 | 243
RX | 63,691 | 65.5 | 7 | 133
Measured rails: TX 3.07 W / RX 3.44 W
PL + PS + DDR; excludes RF and input conversion losses.
PL frame latency: 67.5 ms
Chart: 
| Frame
Encode 38.20 ms | 38.2
Transfer 2.90 ms | 2.9
Decode 26.39 ms | 26.39
Encode 38.20
Transfer 2.90
Decode 26.39
Live PHY diagnostics
DeepJSCC: TCCN 2019. DeepJSCC-Q: JSAIT 2022. Developed with Claude Code and Codex under human direction.
Notes: A4 edition reflowed for print readability from the approved A0 poster. Text is larger, repeated statements are consolidated, and all archived scientific evidence is retained.
All photographs, reference images and reconstructions are repository assets. No image content has been synthesized or retouched.
PSNR chart: data/measurements/psnr_snr/k0802_v3_da.json, results[].snr_da_db against results[].psnr_shown, separately for mode jscc and sscc. Each point is the archived measurement window mean.
Image comparison: decoded_img/tx_reference.png and jscc/sscc_00.00db_p0.png, _20.00db_p0.png, _24.00db_p0.png, _32.00db_p0.png. These suffixes denote TX additional attenuation, not SNR. Labels 32.3,17.4,13.1,5.5 dB are mean SNR across the two schemes at matching attenuation. SSCC has no decoded image at 32 dB attenuation; the gray field is a failure placeholder, not a recovered image. PSNR/SSIM are representative single-frame values, not curve means.
Main gain claim: 31.99-28.23=3.76 dB, rounded to 3.8 dB. This is high-SNR performance on the single DIV2K 0802 image under matched PHY and 32768 complex symbols/image. It is not a dataset-wide gain or a fixed gain at every SNR.
Latency source: report/sections/30_results.md, table 3-6. Medians: encoding 38.20ms, transfer 2.87ms, decoding 30.39ms, separately measured PL total71.47ms. Transfer includes frame buffering, air transmission, synchronization and equalization. Pure airtime2.748ms. PL latency excludes application and display latency. Throughput30fps is possible because frames overlap in the layer pipeline.
Resource source: report/sections/30_results.md table3-1 and build/reports/tx_utilization.rpt, rx_utilization.rpt routed totals. Power source: data/measurements/power/tx_rails.json and rx_rails.json. Values3.06/3.71W sum selected PL,PS,auxiliary andDDR rails. RF daughterboards and12V input conversion losses excluded.
Model/architecture source: report/sections/22_hardware.md. Line buffering abstraction is per convolution engine, not a replacement for the system PHY frame buffers. Full intermediate feature maps are not stored between CNN layers.
Research references: E. Bourtsoulatze, D.B. Kurka, D. Gunduz, Deep Joint Source-Channel Coding for Wireless Image Transmission, IEEE TCCN,2019. T.-Y. Tung,D.B. Kurka,M. Jankowski,D. Gunduz, DeepJSCC-Q, IEEE JSAIT,2022.
Layout references consulted: https://mitcommlab.mit.edu/aeroastro/commkit/research-posters/ and https://mitcommlab.mit.edu/be/2023/09/27/toward-an-evenbetterposter-improving-the-betterposter-template/ . No external artwork copied.