## Slide 1: INTRODUCTION
Radio telescopes use wireless radio reception, measurement, and analysis of celestial radio signals to explore the radio window of celestial bodies after the optical window.
A typical radio telescope system consists of an antenna system, a receiver analog front-end system, a data processing and recording system. Most of the current receiver systems have the capability of accumulate integration, FFT transformation, and correlation calculation, but cannot retain the raw data of the radio signals, Lost a lot of temporal information.
Key technical issues addressed:
1. Signal acquisition, High-performance ADC (Analog-to-Digital Converter) device.
2. Data receiving and processing, AMD-Xilinx 7 series Zynq System on a Chip (SoC) devices.
3. Data transmitting, SERDES (Serializer/Deserializer) Interface with GTX for 10G linerate.
4. Data storing, Dedicated server with disk array and RNIC support.
Title ：Times New Roman Size：24
Typical application case
D
E
S
I
N
G
C
R
E
A
T
I
V
E
Hao Zhang, Zian Zhan, Jiale Ji
On board test by AMD ZYNQ7000
China Three Gorges University,
Hubei Province
R
E
S
U
L
T
SFP+ interface is driven directly by GTX, can be programmed by users to support various communication protocols. This high degree of programmability ensures maximum compatibility with both existing and future communication devices, thereby reducing the cost of device deployment and iterative updates.
Raw data storage requires a significant amount of storage bandwidth. The limitations of current storage devices necessitate the need to build disk arrays that can support high-bandwidth data storage.
System Architecture
High-speed Acquisition Card:
1. Sampling and Quantization of Analog Signals;
2. Receiving and Handling data from ADC;
3. Transporting data to next work platform;
Optical Communication Receiver Card:
1. Communicating with the acquisition card;
2. Receiving and Handling data from SFP+ with protocol such as Ethernet, Aurora and so on;
3. Acting as an assistant to speed up the data processing workflow;
4. Collaborating with the server for data uplink and downlink;
Font: Calibri(Body) Size:11 Size:11
Team Member Names Font: Times New Roman Size:12
作品实物缩略图
作品测试平台信息
校徽
校名
系统框图，关键创新点
测试结果，性能，展望
背景，关键信息摘要