## Slide 1: INTRODUCTION
GlideLink: Real-Time DeepJSCC-Q
Image Transmission on AMD FPGA
D
E
S
I
G
N
C
R
E
A
T
I
V
E
Cunxi Fan, Zhongyu Wang, Junxian Yang
On-board test: RX (left), TX (right)
AMD Zynq UltraScale+ MPSoC
University of Electronic Science
and Technology of China,
Sichuan Province
R
E
S
U
L
T
Live video from drones, robots and remote cameras must cross radio links whose SNR changes from moment to moment. Separate source-channel coding (SSCC) compresses the image with JPEG and adds a channel code: below the code threshold, bit errors propagate through the variable-length code and the whole image is lost (the cliff effect); above it, quality no longer improves.
Typical application case
Camera
drone / robot
Encoder
FPGA, TX
Radio channel
noise, fading
Decoder
FPGA, RX
Display
live view
Deep joint source-channel coding (DeepJSCC) maps pixels directly to channel symbols with a pair of CNNs, so image quality follows the SNR smoothly. DeepJSCC-Q (Tung et al., JSAIT 2022) restricts the symbols to a QAM constellation that a standard digital PHY can carry, but it is computation-heavy and the receiver must pass undecided soft symbols to the decoder.
GlideLink builds a complete real-time link on two AMD Zynq UltraScale+ MPSoC boards (PYNQ-ZU) with AD9361 radios. The DeepJSCC-Q encoder, the decoder and an 802.11a-like OFDM PHY all run in the PL and send 256 × 256 RGB images at 30 fps over the air. The PS captures camera frames, sets up the radios and shows the live link on a touch screen.
Key technical issues: fitting a 1.15-GMAC-per-frame CNN codec into one FPGA at 30 fps with all weights on chip; synchronizing and tracking 683-symbol OFDM frames precisely enough for soft-symbol decoding; and a fair over-the-air comparison with JPEG + LDPC on the same PHY.
TX board PYNQ-ZU (xczu5eg)
PS
4× Cortex-A53, Linux: camera, radio setup
PL
CNN encoder, OFDM TX, LDPC encoder
USB camera
USB
AD9361
RF card
AXI
FMC
RX board PYNQ-ZU (xczu5eg)
PS
A53 + Mali-400 GPU: GUI, web page
PL
OFDM RX, CNN decoder, LDPC decoder
Touch screen
Phone
DP
Wi-Fi
AD9361
RF card
AXI
FMC
over the air
Ethernet: TX preview, control
System Architecture
Key innovations and technical issues addressed:
1. Streaming CNN accelerator: W8A12 integer layers on 64 convolution engines in a layer pipeline at 250 MHz; all weights and activations stay on chip, no DDR traffic.
2. Asymmetric shallow decoder: trained jointly with the encoder, it needs 1/102 of the original multiply-accumulates. The codec does 5.2× the workload of a published FPGA DeepJSCC (GLOBECOM 2025) with fewer DSPs and BRAMs.
3. Soft-symbol OFDM PHY: 683-symbol frames with PN scrambling and second-order SFO/CPE tracking; equalized I/Q go to the decoder without hard decisions.
4. Live system: camera to touch screen with live PSNR, constellations and a 3-D channel view on the Mali-400 GPU.
Over-the-air PSNR (DIV2K 0802, 32,768 64QAM symbols per image)
Chart: Over-the-air SNR (dB)
| 2.94 | 4.94 | 5.9 | 7.03 | 8.43 | 9.3 | 10.49 | 11.48 | 12.48 | 13.02 | 13.74 | 14.18 | 15.76 | 16.33 | 17.03 | 17.36 | 17.38 | 18.45 | 18.91 | 19.54 | 19.68 | 20.79 | 21.31 | 22.48 | 23.1 | 23.24 | 24.49 | 26.5 | 27.69 | 29.56 | 31.97 | 34.43 | 35.2 | 36.14 | 36.49
DeepJSCC-Q | 23.51 | 25.58 | 26.94 | 28.22 | 29.1 | 29.77 | 30.4 | 30.72 | 30.96 | 31.01 | 31.22 | 31.46 | 31.49 | 31.68 | 31.74 | 31.79 | 31.8 | 31.87 | 31.91 | 31.94 | 31.95 | 32 | 32.03 | 32.07 | 32.09 | 32.1 | 32.13 | 32.16 | 32.17 | 32.19 | 32.2 | 32.21 | 32.21 | 32.21 | 32.21
JPEG + LDPC (SSCC) | 9.62 | 9.54 | 9.59 | 9.65 | 9.64 | 14.04 | 9.5 | 9.12 | 9.34 | 27.78 | 28.3 | 28.15 | 25.04 | 28.99 | 29.18 | 29.34 | 29.42 | 29.42 | 29.42 | 29.42 | 29.42 | 29.34 | 29.42 | 29.42 | 29.42 | 29.42 | 29.42 | 29.42 | 29.42 | 29.42 | 29.42 | 29.42
DeepJSCC-Q is 2.8 dB above JPEG + LDPC at high SNR and still gives 23.5 dB at 2.9 dB SNR, while the baseline fails abruptly at 16 to 19.5 dB.
30 fps for 10 min (18,020 frames), 67.5 ms PL end-to-end latency
Design | LUT | BRAM36 | DSP | WNS (ns) | Power*
TX | 54,241 | 104.5 | 243 | +0.082 | 3.07 W
RX | 63,699 | 65.5 | 133 | +0.307 | 3.44 W
* measured, PS + PL + DDR; xczu5eg after routing